## Slide 1
Emotion Augmentation through Affective Haptics and Visual Stimuli
Dzmitry Tsetserukou
Alena Neviarouskaya
Workshop on Affective Haptics

## Slide 2
Introduction
Communication is a process of transferring information (e.g., facts, thoughts, opinions, emotions) from one person to another.
Channels of face-to-face communication:
Verbal:
spoken words
prosodic features (intonation, stress, pitch, loudness, etc.)
Nonverbal:
gaze and eye movements
facial expressions
tints of facial skin
gestures
body postures
touch
“Emotion is what gives communication life. A conversation between emotionally involved partners is bright and lively, but a meeting without feeling is deadly dull.”
Sally Planalp, 1999

## Slide 3
Problem statement
Computer-mediated communication occur via computer-mediated formats , such as e-mail, Instant Messenger, chat room, online 3D virtual world.
With respect to emotional communication, conventional mediated systems usually
support only simple textual cues like emoticons or abbreviations
lack visual emotional signals such as facial expressions and gestures
support only manual control of expressiveness of graphical representations of users (avatars)
completely miss such important channel of social communication as sense of touch
Second Life
Yahoo! IM

## Slide 4
The philosophy behind iFeel_IM! (intelligent system for Feeling enhancement powered by affect sensitive Instant Messenger) is
“I feel [therefore] I am!”
Emotional Telepresence, technology that lets users feel emotionally as if they were present and communicating at a remote physical location.
iFeel_IM!: communication system with emotion enchancing garment

## Slide 5
Architecture of iFeel_IM!
HaptiHeart HaptiHug HaptiTickler HaptiBatterfly
HaptiTemper and HaptiShiver
chat text
3D world Second Life
emotion: intensity
Web-based interface of Affect Analysis Model
PC of each user
Chat log file
Haptic Devices Controller
D/A
Driver box

## Slide 6
Affect Analysis Model: recognition of emotions from text
Test for emoticons, abbreviations, acronyms, interjections, “?” and “!” marks, repeated punctuation and capital letters
Sentence
Estimation of resulting emotion state
Sentence pre-processing for parser
Symbolic cue analysis module
Emoticon or em abbr.
“yes” “no”
Sentence annotated by emotion
emotion category: intensity emotion category: intensity
Syntactical structure analysis module
Stanford Parser
Parser output processing
output of the parser
Word-level analysis module
Phrase-level analysis module
Sentence-level analysis module
I stage
II stage
V stage
III stage
IV stage
Affect database
Emotions: Anger, Disgust, Fear, Guilt, Interest, Joy, Sadness, Shame, Surprise

## Slide 7
Gold standard | Measure | Fine-grained categories |  |  |  |  |  |  |  |  | 
 |  | Neutral | Anger | Disgust | Fear | Guilt | Interest | Joy | Sadness | Shame | Surprise
AAM with Stanford Parser |  |  |  |  |  |  |  |  |  |  | 
2-3 annotators agreed (656 sentences) | Accuracy | 0.649 |  |  |  |  |  |  |  |  | 
 | Precision | 0.30 | 0.77 | 0.64 | 0.74 | 0.71 | 0.61 | 0.83 | 0.74 | 0.50 | 0.76
 | Recall | 0.55 | 0.34 | 0.70 | 0.80 | 0.55 | 0.81 | 0.71 | 0.64 | 0.67 | 0.72
3 annotators agreed (249 sentences) | Accuracy | 0.751 |  |  |  |  |  |  |  |  | 
 | Precision | 0.15 | 0.92 | 0.83 | 0.87 | 0.80 | 0.50 | 0.96 | 0.88 | 0.50 | 0.82
 | Recall | 0.75 | 0.65 | 0.56 | 0.83 | 0.67 | 0.75 | 0.78 | 0.74 | 0.33 | 0.82
AAM with Connexor Machinese Syntax |  |  |  |  |  |  |  |  |  |  | 
2-3 annotators agreed (656 sentences) | Accuracy | 0.726 |  |  |  |  |  |  |  |  | 
 | Precision | 0.46 | 0.83 | 0.63 | 0.76 | 0.75 | 0.56 | 0.87 | 0.78 | 0.57 | 0.85
 | Recall | 0.55 | 0.41 | 0.73 | 0.84 | 0.68 | 0.88 | 0.83 | 0.72 | 0.89 | 0.77
3 annotators agreed (249 sentences) | Accuracy | 0.815 |  |  |  |  |  |  |  |  | 
 | Precision | 0.26 | 0.92 | 0.83 | 0.91 | 0.83 | 0.44 | 0.95 | 0.88 | 0.67 | 0.86
 | Recall | 0.75 | 0.65 | 0.56 | 0.88 | 0.83 | 0.88 | 0.88 | 0.79 | 0.67 | 0.82
Evaluation of the Affect Analysis Model
Experimental dataset: 700 sentences from Weblog Data Collection
3 human annotators

## Slide 8
EmoHeart
Joy Sadness
Anger Fear
Percentage distribution of sentences

## Slide 9
Affective haptic devices activated in iFeel_IM!
Affective haptic devices worn on a human body
HaptiHug
HaptiHeart
HaptiTemper
HaptiButterfly
HaptiTickler
Hapti
Shiver
Back side
Front side
We selected four distinct emotions: ‘Anger’, ‘Fear’, ‘Sadness’, ‘Joy’.
Emotion elicitation implicitly (HaptiHeart, HaptiButterfly, HaptiTemper, and HaptiShiver).
Evoking affect in a direct way (HaptiTickler).
Sense of social touch (HaptiHug) for influencing on the mood and providing some sense of physical co-presence.

## Slide 10
HaptiHug: the way of realistic hugging over distance
Real life hugging Second life hugging HaptiHug
In a real world, whenever one person interacts with another, both observe, perceive and interpret each other’s emotional expressions communicated through a variety of signals.
Among many forms of physical contact, hug is the most emotionally charged one. It conveys warmth, love, and affiliation.
Human body
Pressure
Soft Hand
Pressure
Couple of motors
Pressure
Direction of belt tension
Soft Hand
Motor holder
Direction of belt tension
Pressure distribution
Parameters | Plain Hug
Pressure on male back side, [kN/m2] | 1.4
Pressure on chest, [kN/m2] | 2.3
Average duration, [sec] | 1.98
HaptiHug

## Slide 11
HaptiHeart enchancing our emotions
Of the bodily organs, the heart plays a particularly important role in our emotional experience.
We developed heart imitator HaptiHeart to produce special heartbeat patterns according to emotion to be conveyed or elicited.
The pre-recorded sound signal with low frequency generates the pressure on the human chest through vibration of the speaker surface.
HaptiHeart
Heart-shaped Speaker Case
Flat Speaker

## Slide 12
HaptiButterfly and HaptiTickler : devices for positive emotions
The idea behind HaptiButterfly device is to reproduce effect of “Butterflies in the stomach” (fluttery or tickling feeling in the stomach felt by people experiencing love) by means of the arrays of vibration motors attached to the abdomen area of a person.
We developed HaptiTickler with the purpose to evoke positive affect (joy emotion) in a direct way by tickling the ribs of the user.
Vibration motor
Plastic frame
Holder
Revolute joint
Large vibration motor (little finger)
Large vibration motor (index finger)
Small vibration motors (middle and ring finger)
HaptiButterfly
HaptiTickler
Video

## Slide 13
Haptic device | Emotions |  |  |  | Social Touch
 | Joy | Sadness | Anger | Fear | 
HaptiHeart |  | 83.3% | 66.7% | 100% | 
HaptiButterfly | 83.3% |  |  |  | 
HaptiTickler | 100% |  |  |  | 
HaptiHug | 100% |  |  |  | 100%
The results of the user study revealed that the devices generated the corresponding emotion successfully.
User Study

## Slide 14
Social pseudo-touch (animation) increases the perception:
Perception of hugging force
Perception of heartbeat
Tickling

## Slide 15
Objectives and novelty:
Portable communication system with wearable affective haptic devices driven by user’s finger gestures applied to avatar.
Novel tactile language (haptish) for avatar-mediated communication.
Implementation:
Four basic tactile gestures control wearable devices (HaptiHug, HaptiHeart, HaptiTickler, HaptiShiver) and sensors (microphone, skin conductivity)
Haptinoid: bilateral tactile interaction with avatar through haptic gestures
Hug (Pinch)
Heartbeat
(Double Tap)
Tickling
(Flicking)
Frightening
(Continuous tap)

## Slide 16
BodyTwitter: feel and see your friend’s heartbeat
The purpose of the BodyTwitter is to engage people into communication by transmitting their heartbeats, body temperature online. So that friends can feel their physical presence while being apart.
HaptiHeart
Microphone with preamplifier
Temperature sensor
HaptiHeart with sensors
Touch panel

## Slide 17
Objectives and novelty:
Making user-to-user reflexology foot massage remotely through touch panel.
Enhancing not only health condition, but also social connection between people by means of remote massage.
Implementation:
Slipper-shaped massager with the DC servo and vibration motors to produce the haptic stimuli on the user’s foot.
Touchable application with image of partner’s footprint.
Foottager: touch panel mediated footprint massager

## Slide 18
Thank you!